## Slide 1: FeRRy
RF-aware mission planning for federated learning with drones as data mules
Results overview · IPDPS 2027 submission · October 2026
Notes: FeRRy stands for Federated RF-aware Routing. It plans drone (UAV) missions that carry federated-learning updates to and from devices that cannot reach the server. Plan for the talk: the problem and the idea, related work, the two methods that matter (the two decision clocks and the joint RL model), how we tested it, and then the results, including the limits we measured.

## Slide 2: FeRRy in one slide
THE SHORT VERSION
Drones carry model updates to devices that can't reach the server. FeRRy decides how far each drone's radio reaches.
27–31%
sooner to target accuracy
6 devices, 1 drone, against each of 7 schedulers
~26%
fresher model updates
under tight flight budgets: update age 0.78 vs 1.06–1.07 missions
1.5 s
to plan a mission
for 96 devices on one host
Why it wins: the plan picks a long-reach narrow band, cutting flight between stops from ~140 s to 15 s.
Where it falls short: 3 in 10 tight-budget missions finish late, and it plans as if every device's update is already trained and waiting.
Notes: If you remember one slide, it is this one. Headline: with six devices and one drone at a moderate budget, FeRRy reaches the target accuracy 27 to 31 percent sooner than each of seven baseline schedulers. Under tight budgets it keeps model updates about a quarter fresher than age-of-information schedulers. Planning is cheap: 1.5 seconds for 96 devices. The reason is simple: FeRRy's plan picks a narrow radio band that reaches far, so the drone barely has to fly between stops. We also report where it falls short. First, under tight budgets 3 in 10 missions finish late, because the plan prices the average radio signal and real signal dips make transfers take longer. Second, the plan assumes every device's update is ready when the drone arrives; when devices need time to train, the drone comes back too soon and often finds nothing ready. Slide 19 explains both.

## Slide 3: When the network fails, FL stalls
INTRODUCTION
Federated learning (FL) keeps raw data on devices, but it assumes every device can reach the server.
Where it matters
Disaster response, wildfire monitoring, farms and tactical operations: places with sparse or damaged infrastructure.
What goes wrong
Links are denied, disrupted, intermittent or limited (DDIL). Devices out of range are skipped again and again.
The result
Updates are lost and rounds stall. In our tests, FL over the degraded link merged 0.5 updates per round and stalled at 68.6% accuracy.
✕
✕
✕
edge server
out of range
Notes: FL lets devices train a shared model without sending their raw data, but every device still has to reach the server. In disaster zones, wildfires or tactical settings, that fails: connectivity is denied, disrupted, intermittent or limited. Devices out of range are skipped repeatedly, their updates are lost, and rounds stall. We measured this directly: with no drone, FL over the degraded link merged half an update per round and ended at 68.6 percent accuracy, barely above the 66.7 percent you get by calling every network flow benign. So the gap is not faster FL communication; it is FL that keeps going when the network is fragmented.

## Slide 4: Drones carry updates; reach is a choice
INTRODUCTION
A drone acting as a data mule flies updates between devices and the server, on a limited flight budget.
Wide band (20 MHz): fast, short reach
Reaches 60 m and transfers quickly. Many stops, so most of the mission is spent flying between them.
Narrow band (1.4 MHz): slow, long reach
Reaches 232 m but transfers slowly. One stop can cover the field, so the drone hovers longer but flies far less.
Which one wins depends on how many devices there are, where they are and how much time is left. So FeRRy picks the band and the route together, before every flight.
Narrow band
1.4 MHz · 232 m
Medium band
5 MHz · 120 m
Wide band
20 MHz · 60 m
Test field
200 × 200 m
Device
6 per field here
Notes: Drones acting as data mules can fly model updates between isolated devices and the server. But a drone has limited flight time, and its radio decides how far it reaches. The key observation: the radio band is itself a decision. Same carrier, same transmit power. A wide 20 MHz band transfers fast but only reaches about 60 m, so the drone needs many stops and spends most of its time flying. A narrow 1.4 MHz band reaches about 232 m: one stop can cover the whole field, at the cost of longer transfers while hovering. Rings are drawn to scale over the 200 by 200 m test field. Which band wins depends on the number of devices, their positions and the time left, so FeRRy chooses band and route together before each flight.

## Slide 5: What the paper contributes
INTRODUCTION
Four contributions, from the core idea to how we evaluated it.
1
Reach as a mission decision
The radio band (how far, how fast) is chosen jointly with the route under the flight budget.
2
Two clocks, bounded learning
One feasibility test gates a plan at the dock and the decisions at each stop; learning only ranks what the test admits.
3
Prototype and simulator
Separate processes over TCP train a real model; FerrySim, built from the same code, trains the learned parts and plans for up to 96 devices.
4
A pre-registered comparison
Seven whole schedulers, paired seeds, multiplicity correction; we report wins, null results and limits.
Notes: Four contributions. One: we treat the contact band, which sets how far a drone reaches and how fast it transfers, as a decision made jointly with the route under a mission budget. Two: a two-clock design. The same feasibility test gates the plan made at the dock and the decisions made at each stop in flight. Learning is bounded: it only ranks options the test already admits. Three: a multi-process prototype that trains a real model, and FerrySim, a simulator built from the same code, which trains the learned parts and scales to 96 devices. Four: a pre-registered comparison against seven complete schedulers, with paired seeds and multiplicity correction. We report where FeRRy wins, why, which parts show no effect, and where it falls short.

## Slide 6: Prior work solves pieces of the problem
RELATED WORK
Five lines of research each cover part of what a drone-carried FL system needs.
Line of work | What it does | What it leaves out
Hierarchical and relay FL | Aggregates at edge servers; relays updates over unreliable links (HFL, delay-aware HFL, collaborative relaying) | Assumes a network path eventually exists
UAV-assisted FL | A UAV acts as a mobile server or orchestrator; FedEx physically carries models (closest precedent) | Fixed tours and a fixed radio; no deadlines or in-flight changes
RF-aware UAV trajectories | Learns routes, channels and power from signal, energy and deadlines (multi-UAV DRL, MAPPO) | Not tied to the value of FL updates
Client selection and freshness | Chooses participants by deadline, utility or age (FedCS, Oort, age-of-information, Whittle index) | Ignores the flight and radio cost of reaching a device
Async and hierarchical aggregation | Down-weights late, stale updates (FedBuff, Async‑HFL) | Updates arrive over the network, not by flight
Notes: Five lines of prior work, each solving part of the problem. Hierarchical and relay FL aggregate at the edge and forward updates over unreliable links, but assume some network path eventually exists. UAV-assisted FL brings in mobility. The closest precedent is FedEx, where mobile transporters physically carry models. But FedEx uses preplanned tours and fixed radio conditions, with no deadlines or in-flight adaptation. RF-aware trajectory learning is well studied; we do not claim it as new. What differs is that in FeRRy the radio choice changes whether and how long an FL update takes to transport. Client selection and freshness methods such as FedCS, Oort and age-of-information scheduling rank devices, but ignore the physical cost of flying to them. Asynchronous aggregation such as FedBuff and Async-HFL handles stale updates, but assumes they arrive over the network rather than by flight.

## Slide 7: The gap no prior work closes
RELATED WORK
Even FedEx, the closest precedent, does not tie radio reach and deadlines to in-flight route changes.
Approach | Physical model transport | Explicit RF decision | Route decision | Deadline / freshness aware | In-mission replanning | Joint FL + mobility / RF
Hierarchical FL | — | — | — | — | — | —
FedCS / Oort | — | — | — | ✓ | — | —
UAV multi-community FL | — | — | ✓ | partial | — | ✓
FedEx (transporters) | ✓ | — | ✓ | partial | — | ✓
Model-aided multi-UAV RL | — | partial | ✓ | — | ✓ | —
Deadline-aware multi-UAV | — | partial | ✓ | ✓ | ✓ | —
UAV asynchronous FL | — | partial | ✓ | ✓ | — | ✓
FeRRy (ours) | ✓ | ✓ | ✓ | ✓ | ✓ | ✓
Notes: This matrix condenses Table 1 of the paper. Each row is a representative approach; the columns are the six capabilities a drone-carried FL system needs. Prior work covers some columns: FedEx has physical transport and route decisions; the multi-UAV learning work has RF awareness and in-mission re-planning; client selection has deadlines and freshness. No prior approach couples them: RF-dependent reach and service time, together with per-device deadlines and in-mission route changes, all under a finite mission budget. That coupling is FeRRy's distinction, not any single column on its own.

## Slide 8: How a FeRRy mission works
METHODS
One edge server, one or more drones, and static field devices that train offline between visits.
1
Plan
At the dock: choose the radio band and the route.
2
Collect
Pass 1: fly the route, hand over the model, pick up each device's update.
3
Merge on board
Average the updates; weight stale ones down.
4
Upload
The server merges across drones into the next global model.
5
Deliver
Pass 2: bring the new model to every device.
Three layers feed every decision
L1 · RF link prices
Range, transfer rate and time per stop for each band
L2 · Scheduling decides
Who is served, which band, what order, and when to re-plan
L3 · Federated learning values
Update age, merge weight, and how overdue each device is
Notes: A mission has two passes. At the dock, the drone plans: it picks a radio band and a route. In Pass 1 it flies the route, gives each device the current model and picks up the device's prepared update. It merges those updates on board, weighting stale ones down, flies home and uploads. The server merges across drones into the next global model. In Pass 2 the drone delivers that new model to every device, so each later update has a known base version, and therefore an age. A mission budget bounds Pass 1: the plan and every in-flight check require landing and upload within the budget. Three layers feed each decision. The RF layer prices options: range, rate and dwell time. The scheduling layer decides. The FL layer supplies value: how old an update is, how much it counts, and how overdue a device is.

## Slide 9: Two decision clocks
METHODS · DECISION CLOCKS
FeRRy decides at two time scales, and the same feasibility test gates both.
Plan clock
at the dock, once per mission
Demand and urgency weights
Choose a band class
Group devices into stops at its range
Search routes
Feasibility test, then commit
Flight clock
at every stop in Pass 1
Measure the signal on each band
Choose band and next stop
Feasibility test
Serve the devices (dwell)
Still fits?
If not, re‑plan
commit plan
Why plan band and route together?
The band fixes the range, the range fixes the stops, and the stops fix the route.
Why re-decide in flight?
Interference changes over about one leg. Hard gates always run first; learning only ranks what they admit.
Notes: This is the core of the method: two decision clocks. On the plan clock, once per mission at the dock, the drone chooses a band class and a route together. They have to be chosen together: the band fixes the contact range, the range fixes how devices group into stops, and the stops fix the route. For each band class it clusters devices into stops at that range, searches routes (exact search up to six devices or stops, local search beyond), and commits the plan that serves the most urgency weight, with time and energy breaking ties. On the flight clock, at each stop in Pass 1, the drone measures the actual signal on each band and can change the band and the next stop. Then it serves the devices. If the remaining route no longer fits the budget, it re-plans by trimming. Both clocks share one feasibility test, highlighted in orange. Hard gates always run before any ranking, so a learned rule can only choose among options the test admits.

## Slide 10: One feasibility test gates every decision
METHODS · DECISION CLOCKS
It checks the plan, every departure, every re-plan and every in-flight choice.
A stop is admitted only if…
1
Its devices finish before their deadlines
2
The drone can still fly home and upload within the mission budget
3
The energy fits
arrive = now + distance ÷ speed
finish = arrive + Σ dwell (bytes ÷ rate on the band)
home = finish + return + upload ≤ budget
The plan prices the mean signal, so real missions can run longer: the source of the overruns we report.
Adaptive deadlines
A device's window shrinks after a clean contact (×0.8) and widens after a miss (×1.25 or ×1.5), within limits.
Coverage weight
Weight ≈ (missions since last served)². The plan serves the most weight; time and energy break ties.
Age cap
A device skipped for 2 missions must be served, adding a hover stop just for it if needed.
Stale-aware merges
Update weight = examples × 1/(age + 1), on the drone and again at the server.
Notes: One predicate decides whether a stop may be served next, and it is the only admission rule. It computes when the drone would arrive, when it would finish serving the stop given the transfer rate on the chosen band, and when it would be home with the upload done. The stop is admitted only if the devices meet their deadlines, the drone is home within the budget, and the energy fits. Four ingredients feed it. Deadlines adapt per device: they tighten after a clean contact and loosen after a miss. A coverage weight grows roughly with the square of how many missions a device has gone unserved, so neglected devices become urgent. An age cap forces service after two skipped missions. And merges weight each update by its examples and by one over its age plus one. One caveat: the planner prices the mean signal, not its variation, so real missions can run longer than planned. That is where the budget overruns in the results come from.

## Slide 11: Joint RL model: band + next stop together
METHODS · JOINT RL MODEL
At each stop the flight slot can change the band and the next stop. FeRRy has three ways to fill it.
F · commit
Fly the plan's band and order; no per-stop change.
FX · fixed rule
Fastest band that still reaches the planned devices; nearest stop that keeps the plan feasible.
FQ · learned
A masked double DQN scores each (band, next stop) pair and picks the best allowed one.
State
Signal per band, here and at the next stop
Dwell time
Deadline slack
Plan ages
Mission time and energy left
Interference phase
Masked double DQN
next stop
A
B
C
D
narrow
✕
medium
best
✕
wide
✕
✕
✕
Illustration: gray pairs are masked out
Mask
Allowed only if the band still reaches the planned devices and the rest of the flight passes the test; if none is, use FX.
Reward
Merge weight collected minus a time cost; promised devices left unserved are charged at the end.
Training
Trained in FerrySim, the simulator built from the same code (discount γ = 0.75).
Notes: The joint RL model lives on the flight clock. At each stop the drone has a slot where it may change two things together: the band to serve on, and which stop to fly to next. That pair is the joint action. We built three ways to fill that slot. F leaves it empty and flies the plan. FX is a fixed rule: the fastest band that still reaches the planned devices, and the nearest remaining stop that keeps the plan feasible. FQ is learned: a masked double DQN scores every band-and-next-stop pair. Its state includes the signal on each band here and at the next stop, dwell time, deadline slack, plan ages, mission time and energy left, and the interference phase. The mask is the key safety property: a pair is allowed only if the band still reaches what the plan's band reaches, the stop belongs to the plan, and the rest of the flight passes the feasibility test. If nothing is allowed, it falls back to FX. The reward is the merge weight collected minus a time cost, with a penalty at the end for promised devices that were missed. It is trained in FerrySim. Spoiler for the results: FQ performs like FX, so the learning itself adds nothing measurable; the gain comes from the plan it flies inside.

## Slide 12: How we tested it
EXPERIMENTAL SETUP
A multi-process prototype that trains a real model; flight, radio and energy are simulated.
Prototype
Server, drones and devices run as separate processes over TCP.
Real learning task
Intrusion detector (MLP) on CICIoT2023: 20,000 training flows, 6,000 test flows.
Simulated physics
Flight at 5 m/s, an interference-heavy radio channel, a rotary-wing energy model.
Scenarios
200 × 200 m field; 6, 12 or 24 devices (FerrySim up to 96); 1–3 drones.
How we score it
Primary metric: time to 71% test accuracy (τ = 0.71)
Two budgets: knee (150 s at 6 devices) and stress (half)
20 seeds, paired: same layout, channel and data for every scheduler
A claim: 95% CI excludes 0 and Holm‑corrected p < 0.05
Seven baselines, all on the wide band
H1 (our earlier heuristic)
MAX-AoI
Oort
Whittle index
FedEx route
FedCS
DQN (Chen)
Notes: The prototype runs the server, each drone and each device as separate Python processes talking over TCP, and the devices train a real model: a binary intrusion detector on the CICIoT2023 dataset. Flight time, the radio channel and energy are simulated. FerrySim, built from the same code, trains the learned parts and runs the largest problems. The primary metric is how much simulated time it takes to reach 71 percent test accuracy. That target was fixed in advance from pilot runs; it measures how soon the model becomes useful. Each setting has two budgets: the knee, where more budget stops helping, and a stress budget at half of it. Every comparison is paired by seed, so all schedulers see the same layout, channel and data. A result counts as a claim only if the bootstrap confidence interval excludes zero and the Holm-corrected p-value is below 0.05. We compare against seven complete schedulers: our earlier deadline heuristic H1, MAX age-of-information, Oort, the Whittle index from Cui et al., FedEx's route, FedCS, and a DQN scheduler after Chen et al. All of them fly the wide band.

## Slide 13: FeRRy reaches the target 27–31% sooner
RESULTS · AGAINST THE STATE OF THE ART
Time to 71% accuracy, 6 devices, 1 drone, knee budget (mean of 20 paired trials).
Chart: 
| FeRRy F | FeRRy FX | FeRRy FQ* | FedEx route | Oort | FedCS | Whittle (Cui) | DQN (Chen) | MAX-AoI | H1
Time to target | 194 | 178 | 180 | 264 | 266 | 275 | 280 | 280 | 282 | 282
*FQ was flown later, in an exploratory comparison. F, FX and FQ do not differ from each other.
7 of 7
baselines significantly slower than F
80–90%
of paired seeds: F gets there first
3 drones
every scheduler 52–65 s; FedEx with its own merge 101 s
No drone
0.5 updates per round, 68.6% accuracy (F: 3.5 and 83.1%)
Notes: The headline result. With six devices, one drone and the knee budget, F reaches 71 percent accuracy in 194 seconds; the seven baselines need 264 to 282 seconds. That is 27 to 31 percent faster, every comparison is a statistically significant claim, and F gets there first in 80 to 90 percent of paired seeds. FX and FQ, the per-stop variants, are not different from F. FQ was flown later in an exploratory comparison, marked with an asterisk. Two context points. With three drones every scheduler gets there in about a minute, except FedEx with its own merge rule at 101 seconds. And with no drone at all, FL over the degraded link merges half an update per round and ends at 68.6 percent accuracy, compared with F's 3.5 updates per round and 83.1 percent. Under the tighter stress budget, only the FedEx route is significantly slower; the other baselines trail by 28 to 60 seconds but stay within budget by leaving devices out.

## Slide 14: Why: the right band removes the flying
RESULTS · WHY IT IS FASTER
Every scheduler needs about the same number of rounds (1.65–1.84); FeRRy's rounds are just shorter.
Chart: Mean mission time (s), 6 devices, knee budget
| F (band chosen) | F pinned to narrow | F pinned to wide | FedEx route | H1
Transit between stops | 15.47 | 14.05 | 138.11 | 137.79 | 140
Dwell (transfers) | 107.21 | 109.72 | 10.64 | 10.73 | 10.98
Return, upload, dock | 45.52 | 45.02 | 66 | 66.05 | 72.49
89%
of F's missions fly the narrow band at 6 devices
15 s vs ~140 s
flying between stops, F vs the baselines
≈ 265 s
F pinned to the wide band: no faster than FedEx's route; pinned to narrow, 196 s
Notes: Why is FeRRy faster? Not because it needs fewer rounds: every scheduler reaches the target in about 1.7 to 1.8 rounds with nearly the same number of updates. FeRRy's rounds are shorter. Every baseline flies the wide band, which only reaches devices from nearby, so about 140 seconds of each mission is transit between stops, the red segment. F's plan chooses the narrow band in 89 percent of missions. Its range covers the field from about one stop, so F spends 15 seconds in transit and most of its time transferring (the teal segment). Missions end up 22 to 26 percent shorter. The pinning test confirms the cause: force F onto the wide band and it takes about 265 seconds, the same as FedEx's route. Force it onto narrow and it takes 196 seconds, the same as letting it choose. A caveat for questions: these pinned times are descriptive. The band-pinning study's pre-registered metric was the age of updates, which did not differ.

## Slide 15: The band choice adapts to the field
RESULTS · WHY IT IS FASTER
Share of F's plans flying each band. Few devices and a loose budget favour narrow; many devices, wide.
Chart: 
| 6 devices · knee | 6 devices · stress | 12 devices · knee | 12 devices · stress | 24 devices · knee | 24 devices · stress
narrow (1.4 MHz) | 89.2 | 67.2 | 48.6 | 12.7 | 0.4 | 2.2
medium (5 MHz) | 10.8 | 30.7 | 51.4 | 68.7 | 60.8 | 30.1
wide (20 MHz) | 0 | 2 | 0 | 18.6 | 38.8 | 67.6
Near the best possible
Serves as many devices as an exhaustive search at the knee budget, and 4 points fewer under stress.
No fixed band works everywhere
A denser field or a tighter budget pushes F toward wider, faster bands, so the band is decided per mission.
Notes: The band choice is not a fixed preference for narrow. It adapts. With six devices and the knee budget, F picks narrow 89 percent of the time. As the field fills (the field size stays the same, so it gets denser) and as the budget tightens, F shifts toward medium and then wide. With 24 devices under the stress budget it flies wide in about two thirds of missions. That is the point of treating reach as a decision: no single band is right everywhere. The choice is also close to the best possible. In FerrySim, an exhaustive oracle that tries every plan serves the same number of devices at the knee budget, and only 4 points more under stress.

## Slide 16: It scales, and planning stays cheap
RESULTS · SCALE AND COST
Planner time per mission alone on one host, and time to target as devices and drones are added.
Chart: Planner time per mission (95th percentile at 96 devices: 2.0 s)
| 6 | 12 | 24 | 48 | 96
Plan time | 0.04 | 0.02 | 0.14 | 0.41 | 1.53
24 devices, 1 drone
Knee: F 749 s vs H1 951 s and Whittle 911 s (significant)
Ties FedEx's route at the knee (752 s) and beats it under stress (661 vs 752 s)
At 12 devices no comparison reached significance
Adding drones (12 devices, knee)
486 s
1 drone
226 s
2 drones
151 s
3 drones
Notes: Scale and cost. Planning stays cheap. Alone on one host, a plan takes 0.04 seconds at six devices and 1.5 seconds at 96, with the 95th percentile at 2 seconds. (The small dip at 12 devices is real: the search switches from exhaustive to a cheaper mode as the problem grows.) At 24 devices, F is significantly faster than H1 and the Whittle index at the knee, ties FedEx's route, and beats it under the stress budget, 661 against 752 seconds. At 12 devices no comparison reached significance. Adding drones helps a lot: at 12 devices F's time to target falls from 486 seconds with one drone to 226 with two and 151 with three.

## Slide 17: Fresher updates under tight budgets
RESULTS · DESIGN CLAIMS
Age of updates under the stress budget: missions since each device was last merged (lower is better).
Chart: 
| FeRRy | MAX-AoI scheduler | Whittle index | FeRRy without coverage term
Age of updates | 0.78 | 1.06 | 1.07 | 1.1
All three differences are significant (Holm p ≤ 0.009).
Design choices that matter
Coverage term: without it, rounds closed fall from 99% to 74% (12 devices)
About 26% fresher than age-of-information schedulers
Adaptive backhaul carrier: age 0.88 → 0.69 missions
No measurable effect at our settings
Pinning the band (on age), the dwell term, the age cap over 4 missions, other merge rules (updates almost always arrive fresh), and FedCS- or Oort-style deadlines.
Notes: Fairness and freshness. Under the stress budget, FeRRy's network age of updates is 0.78 missions, against 1.06 for a MAX age-of-information scheduler and 1.07 for the Whittle index. Removing FeRRy's coverage term pushes it to 1.10. All of these are significant. The coverage term also matters for closing rounds: without it, the round-close rate at 12 devices falls from 99 to 74 percent. On a time-varying backhaul, the adaptive carrier controller lowers the age from 0.88 to 0.69, though it sees the signal that decides each loss, so it is close to an oracle. We also report what showed no measurable effect: pinning the band (on age, its effect is on time), the dwell term, the age cap over four missions, alternative merge rules (they tie because collected updates are almost always current), and the deadline forms from FedCS and Oort, which miss slightly more deadlines, but not significantly.

## Slide 18: Learning helps only inside the plan
RESULTS · JOINT RL MODEL
Time to 71% accuracy, 6 devices, 1 drone, knee budget. E3 is a learned DQN scheduler with no plan.
Chart: 
| F (plan only) | FX (fixed rule) | FQ (learned, in plan) | E3 (learned, no plan)
Time to target | 194 | 178 | 180 | 280
Pre-registered test: flat
No discount γ beat γ = 0, and FQ matched FX (and F). FX stays FeRRy's per-stop rule.
Exploratory: FQ vs E3
180 vs 280 s at the knee: 100 s faster (95% CI 63–141 s; Holm p < 0.001). Under stress, 174 vs 211 s, not significant.
Why
FQ inherits the plan's band: 15 s of a 155 s mission is flying, vs 144 s of 228 s for E3. The gain is the plan, not the learning.
Notes: What about the joint RL model? The pre-registered test was flat. In FerrySim no discount factor beat a purely myopic one by the required margin, and in the full system FQ was indistinguishable from the fixed rule FX, and from F. So FX is FeRRy's per-stop rule. We then ran an exploratory comparison, not pre-registered: FQ against E3, a DQN scheduler after Chen et al. that picks every next stop with no plan, on the same 20 seeds. At the knee, FQ reaches the target in 180 seconds against E3's 280: 100 seconds faster, or 36 percent sooner, with a confidence interval of 63 to 141 seconds. Under stress it is faster too, but not significantly. The reason is the plan, not the learning. FQ inherits the plan's band and spends 15 seconds of a 155-second mission in transit; E3 spends 144 of 228. This supports the two-clock structure: plan at the dock, then refine per stop.

## Slide 19: Limits we measured
LIMITATIONS
Two limits matter most, and each comes from something the plan does not price.
Tight budgets: 3 in 10 missions finish late
What happens
Under the stress budget, 30% of F's missions overrun, by about 28 s on a 75 s budget. FedEx's route, which never skips a device, overruns in 85%.
Why
The plan prices the average signal, but interference and shadowing make the real signal dip, so transfers take longer than planned. Most of F's mission is transfer time (85 of 155 s), and nothing re-checks after the last stop.
Next step
Price the signal's variation, or keep slack in reserve.
Training time: updates are not ready
What happens
When devices need time to train, 79% of F's visits find no update ready: 0.7 updates per round instead of 3.5. F reaches the target in 70–75% of trials (H1, FedEx route, FedCS: 85–100%).
Why
The plan assumes every update is waiting. Training (median 68 s) restarts with each new model, and F reaches the field with ~11 s of flying, so it often returns before devices finish. The baselines' ~130 s tours give devices time.
Next step
Add each device's expected training time to the plan.
Also: flight, radio and energy are simulated (real-radio tests await a testbed), and some studies flew 20 of 40 planned trials. With non-IID data, every scheduler reaches the target in about half the trials.
Notes: Two limits matter most, and both come from something FeRRy's plan does not price. First, tight budgets. Under the stress budget (75 seconds for collection at six devices), 30 percent of F's missions finish late. The ones that run late go over by about 28 seconds on average. (Averaged over all missions, including the 70 percent that finish on time, that is 8.5 seconds.) For comparison, FedEx's route, which never skips a device, runs late in 85 percent of missions. The other baselines almost never run late, but they stay inside the budget by leaving devices out: they merge 2.0 to 2.7 updates per round, against F's 3.2. Why it happens: the plan prices the average signal on each band. In flight, interference and shadowing make the real signal dip below that average, the transfer rate drops, and each transfer takes longer than planned. F is especially exposed, because its narrow-band missions are mostly transfer time (85 of 155 seconds), which is exactly the part the signal controls; flying time is fixed by distance. The drone re-checks the budget when it leaves each stop, but nothing re-checks after the last stop, so the last stop's extra time, the return and the upload can push the mission past the limit. FX, which switches to a faster band in flight when the signal allows, runs late less often (24 percent). The fix is to price the signal's variation, or to keep some slack in reserve. Second, training time. In the main experiments a device's update is always ready when the drone arrives. In the training-time study each device needs time to train (median 68 seconds), and it starts over every time it receives a new model. FeRRy's plan does not know this. Because F reaches the whole field with about 11 seconds of flying, it comes back very soon after delivering a new model, often before devices have finished retraining: 79 percent of its visits find nothing ready, and it merges 0.7 updates per round instead of 3.5. The baselines spend about 130 seconds flying their wide-band tours, which gives devices time to finish, so only 21 to 38 percent of their visits find nothing ready. F reaches the target in only 70 to 75 percent of trials, against 85 to 100 percent for H1, FedEx's route and FedCS. A caution: in that study F's time to target looks faster, but only because it is averaged over the trials that reach it. The fix is to add each device's expected training time to the plan. Also: flight, radio and energy are simulated, and several studies flew 20 of their 40 planned trials. With strongly non-IID data, every scheduler reaches the target in about half the trials, and F stays faster than H1 and the Whittle index where both do.

## Slide 20: Takeaways and next steps
1
Reach is a decision.
Choosing the band with the route made FeRRy 27–31% faster to target accuracy.
2
The gain comes from the plan.
Learning inside it matched a fixed rule, and reached the target 36% sooner than a learned scheduler with no plan.
3
Fresh and cheap.
Updates stay about a quarter fresher under tight budgets, and 96 devices plan in 1.5 s.
Next steps
Price channel variation in the plan
Add device training time to the plan
Validate the band trade over the air on a UAV testbed
Coordinate drones that share spectrum and a dock
Notes: Three takeaways. One: treat the drone's reach as a decision. Choosing the band together with the route is what made FeRRy 27 to 31 percent faster. Two: the gain comes from the plan. Learning inside the plan matched a fixed rule, and it reached the target 36 percent sooner than a learned scheduler with no plan. Three: FeRRy keeps updates fresher under tight budgets and plans cheaply, 1.5 seconds for 96 devices. Next steps follow from the limits: price the channel's variation, add training time to the plan, validate over the air on a UAV testbed, and coordinate drones that share spectrum and a dock.